## Slide 1: VHDL for Sequential Logic
ELEC 311
Digital Logic and Circuits
Dr. Ron Hayne
Images Courtesy of Cengage Learning

## Slide 2: D Flip-Flop

## Slide 3: Asynchronous Clear

## Slide 4: Shift Register

## Slide 5: Counter

## Slide 6: Design Example
T-bird Tail Lights
  Left Turn
  Right Turn
  Hazard

## Slide 7: Flashing Sequence

## Slide 8: Flashing Sequence
Left Turn
Right Turn

## Slide 9: Initial State Graph
Mutual Exclusion?
All Inclusion?

## Slide 10: Corrected State Graph
Handles multiple inputs asserted simultaneously

## Slide 11: Enhanced State Graph
Goes into hazard mode as soon as possible

## Slide 12: VHDL Model
entity TBIRD is
port (clock, left, right, haz : in std_logic;
tail : out std_logic_vector (1 to 6));
end TBIRD;
architecture BEHAVE of TBIRD is
type State_type is (IDLE,L1,L2,L3,R1,R2,R3,LR3); signal State, Next_State: State_type; signal input: std_logic_vector(1 to 3);
begin
input <= left & right & haz;

## Slide 13: VHDL Outputs
with State select
tail <= "000000" when IDLE,
"001000" when L1,
"011000" when L2,
"111000" when L3,
"000100" when R1,
"000110" when R2,
"000111" when R3,
"111111" when LR3;

## Slide 14: VHDL Sequential Machine
process (input, State)
begin
case State is
when IDLE =>
case input is
when "010" => Next_State <= R1;
when "100" => Next_State <= L1;
when "--1" => Next_State <= LR3;
when others => Next_State <= IDLE;
end case;
when L1 =>
case input is
when "--1" => Next_State <= LR3;
when others => Next_State <= L2;

## Slide 15: VHDL Sequential Machine
process (SLOW_CLK)
begin
if SLOW_CLK'event and SLOW_CLK = '1' then
State <= Next_State;
end if;
end process;

## Slide 16: Summary
Sequential VHDL
  process
  if-then-else
  case
Design Example